## Slide 1: SNMPv1: Organization and Information Models
 | Subject-NAM | 

## Slide 2: Internet SNMP Management
Internet Engineering Task Force (IETF)
  1990 SNMPv1
  1995 SNMPv2
  1998 SNMPv3
Internet documents:
  Request for Comments (RFC)
  IETF STD Internet Standard
  FYI For your information

## Slide 3
SNMP MIB
RFC 3418
SNMP MIB
RFC 3418
SMIv2
RFC 2578
SMIv2
Conventions
RFC 2579
SMIv2
Conformances
RFC 2580
SNMP MIB
RFC 3418
SNMPv2
Protocol Ops
RFC 3416
`

## Slide 4: SNMP Model
Organization Model
  Relationship between network element, agent, and manager
  Hierarchical architecture
Information Model
  Uses ASN.1 syntax
  SMI (Structure of Management Information
  MIB (Management Information Base)
Communication Model
  Transfer syntax
  SNMP over TCP/IP
  Communication services addressed by messages
  Security framework community-based model

## Slide 5: Two-Tier Organization Model

## Slide 6: Three-Tier Organization Model: RMON
RMON
Remote Monitoring
RMON I
RMON II

## Slide 7: Three-Tier Organization Model: Proxy

## Slide 8: SNMP System Architecture
Network
網路介面
SNMP
UDP
IP
網路介面
SNMP
UDP
IP
網路介面
SNMP
UDP
IP
Manager
Agent
Agent
. . .
Management
Station
Host
Router
Network Elements (NEs)
Network
Management
Protocol
SNMP

## Slide 9: SNMP Services
Four Services
  Get, Set, GetNext, Trap
Five SNMP Messages
  GetRequest, SetRequest, GetNextRequest, GetResponse, Trap
Manager
Agent(s)
Get, Set, GetNext Request
Get Response
Trap

## Slide 10: SNMP Services
Get Request
Get Response
Manager
Agent
GetNext Request
Get Response
Manager
Agent
Set Request
Get Response
Manager
Agent
Trap Request
Manager
Agent
Get
GetNext
Set
Trap

## Slide 11: SNMP Services (cont.)
Get Request:
  Retrieve the values of objects in the MIB of an agent.
Get-Next Request:
  Retrieve the values of the next objects in the MIB of an agent.
Set Request:
  Update the values of objects in the MIB of an agent.
Trap Request
  Report extraordinary events to the manager.

## Slide 12: 4.7 Information Model
Structure of Management Information (SMI) (RFC 1155, RFC 1212)
Managed Object
  Scalar
  Aggregate or tabular object
Management Information Base (RFC 1213)

## Slide 13: Managed Object
Object Type
Object Instance

## Slide 14: Managed Object: Multiple Instances
Object Type
Object Instance

## Slide 15: Object Name
Object is uniquely defined by
  DESCRIPTOR
  OBJECT IDENTIFIER

## Slide 16: Internet Subnodes
directory OBJECT IDENTIFIER ::= {internet 1}
mgmt OBJECT IDENTIFIER ::= {internet 2}
experimental OBJECT IDENTIFIER ::= {internet 3}
private OBJECT IDENTIFIER ::= {internet 4}

## Slide 17
root
ccitt
iso
joint-iso-ccitt
directory
0
1
2
std
reg
authority
member
body
org
0
1
2
3
dod
internet
6
1
1
2
3
4
mgmt
experimental
private
MIB II
system
1
interface
2
at
3
IP
4
ICMP
5
TCP
6
UDP
7
EGP
8
Trans.
10
SNMP
11
1
1
enterprises
1.3.6.1.2.1.2
1.3.6.1.4.1
1.3.6.1.2.1
MIB II
interface
enterprises

## Slide 18: Private MIB Example
Enterprise Number

## Slide 19: SMIv1, SMIv2
SMIv1:
  SMI (RFC 1155)
  Concise MIB (RFC 1212)
  Trap-Type (RFC 1215)
SMIv2:
  SMIv2 (RFC 2578)
  Textual Conventions (RFC 2579)
  Conformance Statements (RFC 2580)

## Slide 20: 4.7.4 MIB-II
MIB-II (RFC 1213) is superset of MIB-I
Objects that are related grouped into object groups
MIB module comprises module name, imports from other modules, and definitions of current module
RFC 1213 defines eleven groups