## Slide 1: Package and Libraries

## Slide 2: Packages Declaration
Collection of definitions of constants, data types, components, and subprograms.
A package serves as a central repository for frequently used utilities, such as component declarations.
The declarations may then be reused by any VHDL model by simply accessing the package.
use WORK.PROJECT_PACK.all;
The architecture accesses the component
declarations in the package”PROJECT_PACK" located in the library WORK via the use clause.
Use clause placed just before the architecture body statement

## Slide 3: Example
package EXAMPLE_PACK is
type SUMMER is (JUN, JUL, AUG);
component D_FLIP_FLOP
port ( D, CK : in BIT;
Q, QBAR : out BIT);
end component;
constant PIN2PIN_DELAY : TIME := 125ns;
function INT2BIT_VEC (INT_VALUE : INTEGER)
return BIT_VECTOR;
end EXAMPLE_PACK;
library DESIGN_LIB; -- library clause
use DESIGN_LIB.EXAMPLE_PACK.all; -- use clause
entity EXAM is ...

## Slide 4: Package Body
Package body is used to store the definitions of functions and procedures that were declared in the corresponding package declaration.
A package body is always associated with a package declaration
Example
package body EXAMPLE_PACK is
function INT2BIT_VEC (INT_VALUE: INTEGER)
return BIT_VECTOR is
begin
-- behavior of function described here
end INT2BIT_VEC;
end EXAMPLE_PACK;

## Slide 5: Example of Package
package LOGIC_OPS is -- package
-- Declare logic operators
component AND2_OP
port (A, B : in BIT;
Z : out BIT);
end component;
component OR3_OP
port (A, B, C : in BIT;
Z : out BIT);
end component;
component NOT_OP
port (A : in BIT;
A_BAR : out BIT);
end component;
end LOGIC_OPS;

## Slide 6: Example of Package Usage
-- entity declaration
entity MAJORITY is
port ( A_IN, B_IN, C_IN : in BIT;
Z_OUT : out BIT);
end MAJORITY;
-- architecture description
-- uses components from package LOGIC_OPS in library WORK
use WORK.LOGIC_OPS.all;
architecture STRUCTURE of MAJORITY is
signal INT1, INT2, INT3 : BIT;
begin
A1: AND2_OP port map (A_IN, B_IN, INT1);
A2: AND2_OP port map (A_IN, C_IN, INT2);
A3: AND2_OP port map (B_IN, C_IN, INT3);
O1: OR3_OP port map (INT1, INT2, INT3, Z_OUT);
end STRUCTURE;

## Slide 7: Library

## Slide 8
There are two reserved library names always available to designers.
–WORK: Predefined library
–STD: The STD contains two packages: STANDARD provides declaration for predefined types (real, integers, Boolean, etc). TEXTIO contains useful subprograms that enables to perform ASCII file manipulations
•library STD; -- declares STD to be a library
•use STD.STANDARD.all;
-- use all declarations in package
-- STANDARD, such as BIT, located
-- within the library STD
A library clause declares WORK to be a library.
library WORK; -- WORK is predefined library

## Slide 9
User-defined libraries: LOGIC_LIB
–Assume the LOGIC_OPS package is located in the LOGIC_LIB library instead of WORK library.
library LOGIC_LIB;
use LOGIC_LIB.LOGIC_OPS.all;
architecture STRUCTURE of MAJORITY is
-- use components in package LOGIC_OPS of library LOGIC_LIB

## Slide 10: Thank u
POONAM
(Astt. Prof. in ECE dept.)
CDLSIET,P.MOTA